## Slide 1
NC-SSM
Voice AI on a $5 Chip
Noise-Conditioned State Space Model
for Edge Keyword Spotting
Interspeech 2026 | CES 2027 | Patent Pending
01

## Slide 2
The Problem
Voice AI is broken at the edge
02
• Expensive Hardware: Current voice AI requires powerful processors, driving up BOM cost and power budget • Noise Failure: Models trained in clean conditions collapse in real-world noise (factory, car, kitchen) • High Latency: DS-CNN-S: 24K params, 53ms latency -- too slow for real-time interaction on MCUs • Power Hungry: Always-on listening drains batteries -- CNNs process every frame even during silence • No Streaming: Conventional models need the full 1-second window before detection begins
53ms
CNN Latency
24K
DS-CNN-S Params
196KB
CNN Feature Maps
66.3%
CNN @ 0dB SNR

## Slide 3
The Solution
Structural noise robustness -- no denoising module needed
03
• SSM Architecture: State Space Models process sequences with O(1) memory per step -- ideal for streaming on MCUs • Noise-Conditioning: 5 mechanisms that adapt model dynamics in real-time based on per-band SNR estimates • Zero Overhead: No separate denoising module, no extra MACs -- noise robustness is built into the architecture • Silence Efficiency: SSM state update costs 0 MACs during silence, enabling 10x battery life improvement • Streaming Native: ~350ms detection for short keywords vs 1053ms for CNN -- instant wake-word response
7.1ms
NC-SSM Latency
7,443
Parameters
720B
Hidden State
77.7%
Accuracy @ 0dB

## Slide 4
Technology
NC-SSM Architecture: End-to-End Noise-Conditioned Pipeline
04
1s Audio
▶
STFT
▶
40-band
Mel
▶
SNR
Estimation
▶
DualPCEN
▶
SSM
Block x2
▶
Classifier
5 Noise-Conditioning Mechanisms
Sub-band
Selectivity
Per-frequency
attention gating
Delta Floor
Conditioning
Adaptive noise
floor estimation
B-base
Conditioning
Dynamic SSM
matrix scaling
Learned
Spectral Gate
SNR-driven
feature masking
Spectral
Subtraction
Noise spectrum
removal

## Slide 5
Performance
Benchmarks on Google Speech Commands v2 (12-class)
05
Model
Params
MACs
Latency
Accuracy
0dB SNR
DS-CNN-S (baseline)
24,000
5.4M
53ms
95.4%
66.3%
NC-SSM (ours)
7,443
0.86M
7.1ms
95.3%
77.7%
NC-SSM-20K (ours)
20,000
2.44M
10.4ms
96.4%
--
5x less latency
vs DS-CNN-S at matched accuracy
10x fewer MACs
NC-SSM-20K vs DS-CNN-S
+11.4% @ 0dB
Noise robustness (clean-trained)

## Slide 6
Competitive Advantage
Why NC-SSM wins at the edge
06
Proven Noise Robustness
Only KWS model with formal structural
noise robustness proof
Instant Streaming
~350ms detection for short words
vs 1053ms for CNN (3x faster)
720 Bytes State
720 bytes hidden state vs 196KB
CNN feature maps (272x smaller)
Zero Silence Cost
0 MACs during silence periods
= 10x battery life improvement

## Slide 7
Business Model
Multiple revenue streams from a single core technology
07
IP Licensing
$0.01-0.05/chip
Per-chip royalty for
NC-SSM core IP
Nano AI SDK
$500-5K/mo
SaaS platform for
custom model training
Custom Wake Word
$10K-50K/project
Turnkey custom keyword
detection solutions
Edge AI Module
BOM $4.80 / Sell $15-30
Ready-to-integrate
hardware module

## Slide 8
Market Opportunity
Riding the edge AI wave
08
$26.8B
Global Voice Recognition (2025)
➡
$50B+
Projected Market (2030)
Always-on edge AI: fastest growing segment
Target Verticals
IoT / Smart Home
Voice-controlled
appliances & hubs
Automotive
In-cabin voice
commands
Wearables
Watches, earbuds,
health devices
Industrial
Factory floor,
hands-free control
Consumer
Electronics
TVs, remotes,
speakers

## Slide 9
Traction & Milestones
From research to production-ready
09
DONE
Interspeech 2026 paper submitted
DONE
CES 2027 demo ready (live inference)
DONE
US + KR patent applications filed
DONE
Working C SDK for ARM Cortex-M7
DONE
FPGA implementation complete
LIVE
Open-source community on GitHub
IP Portfolio
◆ NC-SSM Architecture
◆ DualPCEN Front-end
◆ 5 Noise-Conditioning
Mechanisms
◆ Streaming SSM
Inference Method
◆ Silence-Aware
Power Management

## Slide 10
Deploy Noise-Robust
Voice AI Today
NC-SSM: 7,443 params. 7.1ms latency. Runs on a $5 chip.
Dr. Jin Ho Choi
NC-SSM Project Lead
github.com/nc-ssm
Interspeech 2026 | CES 2027
US + KR Patent Pending
Schedule a Demo
License the IP
Try the SDK
10